## Slide 1: Senegal Sonatel NB-IoT vEPC Technical Solution and Workload

## Slide 2: Backgroud and General Solution:
vEPC is using CUPS platform.
2
3
Use specific APN NBIoT handle the NB-IOT service.
Sonatel is going to deploy trial NB-IOT service. Core network will re-use exist Medina and DC vEPC.
1
Single RAN
G/U/L/NB IoT
IoM Platform
MED vUSN
HLR/PCRF
3rd Application Server
RUF vUSN
MED CGW
MED DGW
RUF CGW
RUF DGW
S11-C
S11-C
S11-U
S11-U
SGi
SGi
SGi
RUF DGW
Internet

## Slide 3: NB-IOT vEPC feature requirement
Exist network analysis:
1. Exist vEPC version is V100R020C05, support NB-IoT feature.
2. NB-IoT license is not exist on vEPC.
Feature request analysis：
CloudUSN CloudUGW
License Item ID | Feature | Description
81202652 LKV2NBPS01 | NB-IoT Platform Software | Mandatory
82207361 LKV2NBFQ01 | NB-IoT Connection Basic Software Level 1 | At least one of them must be selected. If multiple items are selected, the highest-level item takes effect. Mandatory
82207362 LKV2NBFQ02 | NB-IoT Connection Basic Software Level 2 | 
82207363 LKV2NBFQ03 | NB-IoT Connection Basic Software Level 3 | 
82207029 LKV2DNAS01 | Data Over NAS | Optional (mandatory in CP-CIoT scenarios)
82207713 LKV2UPTH01 | NB-IoT User Plane Transmission Holding | Optional (used in UP-CIoT scenarios)
82207026 LKV2M2MS01 | Power Saving Mode | Optional
82207382 LKV2EDRX01 | NB-IoT eDRX Mode | Optional
82207383 LKV2NOIP01 | Non-IP Data Transmission | Optional
82207028 LKV2CELP01 | eNodeB Coverage Level Based Paging | Optional (can be used with LTE Precise Paging)
82206599 LKV2PRPG01 | LTE Precise Paging | Optional (required when deploying eNodeB Coverage Level Based Paging)
82207031 LKV2LPAC01 | Low-Priority Access Flow Control | Optional
82207030 LKV2LTCC01 | Signaling Congestion Control Based on the Back-off Timer | Optional
82207033 LKV2ASCC01 | APN based Signaling Congestion Control | Optional
82207714 LKV2AARC01 | APN Based NB-IoT Access Rate Control | Optional
82207715 LKV2SARC01 | Serving PLMN Based NB-IoT Access Rate Control | Optional
License Item ID | License Item | Description
81202655 LKV3WPNBPS01 | NB-IoT Platform Software (per CloudUGW) | Mandatory
82207421 LKV3WNBSLO01 | NB-IoT Connection Basic Software Level 1(per PDP) | At least one of them must be selected. If multiple items are selected, the highest-level item takes effect. Mandatory
82207422 LKV3WNBSLT01 | NB-IoT Connection Basic Software Level 2(per PDP) | 
82207732 LKV3WNBSL301 | NB-IoT Connection Basic Software Level 3(per PDP) | 
82207072 LKV3WPSDTO01 | Data Over NAS(per PDP) | The license controls the NB-IoT Data Transfer Optimization feature.
82207357 LKV3WNBNIP01 | Non-IP Data Over NAS(per PDP) | 
82207356 LKV3WNBDRX01 | NB-IoT eDRX Mode(per PDP) | Optional (controlling NB-IoT terminal energy saving management)
82206922 LKV3WPSSBT01 | Signalling Congestion Control Based on the Back-off Timer(per PDP) | Optional (controlling access control and coverage enhancement for massive NB-IoT connections)
82207564 LKV3WNBARC01 | APN Based NB-IoT Access Rate Control(per PDP) | 
82207565 LKV3WNBPRC01 | Serving PLMN Based NB-IoT Access Rate Control(per PDP) | 

## Slide 4
NB-IOT vEPC interface variation
Add new logic interface S11-U, use private IP design on CloudUSN and DGW.
S1 、 S10 、 S11 、 S5&S8 、 S6a、NAS interface variation and CDR information is strengthened.
New APN for NB-IoT need to be designed on CloudCGW&DGW.
Logical Interface | VRF | Logical Interface IP | commnet
MED_CloudUSN01 | vEPC_Media |  | use x.x.x.x as the S11-U interface in VUSN
MED_CloudDGW01 | vEPC_Media |  | need provide a logic ip for s11-u interface in dgw that connect to MME
 | vEPC_Media |  | 
DC_CloudUSN01 | vEPC_Media |  | use x.x.x.x as the S11-U interface in VUSN
DC_CloudDGW01 | vEPC_Media |  | need provide a logic ip for s11-u interface in dgw that connect to MME
 | vEPC_Media |  | 
Interface design

## Slide 5: Deploy & Test case
The main actions for deploy：
LLD design for NB-IOT.
2. Create new S11-U interface and configure IP routing between CloudUSN and CloudDGW.
3. Create new DNSN on CloudUSN, point to CloudUGW.
4. Create new APN on CloudCGW, need check with Sonatel if need use specific VPN and IP pool, static IP or dynamic IP for user；
5. Create new VPN and IP route configuration on CloudCGW and PE if use new VPN.
6. Service test and verify.
Test case based on license availability on CloudUSN and CloudUGW ：
IP Data Over NAS
Non-IP MO/MT Data over NAS
3. eNodeB Coverage Level Based Paging (optional)
4. Power Saving Mode Activation (optional)
    5. NB-IoT eDRX Mode Activation (optional)
6. NB-IoT SMS Transmission Over SGs (optional)

## Slide 6: Workload on vEPC
No. | Issue | Due Date
1 | LLD Design of NB-IOT on vEPC. | 5 person/working day
2 | License activation for NB-IOT. | 2 person/working day
3 | S11-U interface integration for NB-IOT. | 4 person/working day
4 | New APN and IP pool integration for NB-IOT. | 4 person/working day
5 | New VPN and IP route configuration on CloudCGW/DGW and PE if use new VPN. | 5 person/working day
6 | Service test and verify. | 8 person/working day
Total |  | 28 person/working day